# ABSTRAK

Priambodo Budi Santoso, 2022. Deteksi Titik Buta(Blind Spot) pada Pengendara Sepeda Motor menggunakan Mikrokontroler Arduino dengan Sensor HC-SR04. Tugas Akhir, Program Studi Teknik Informatika (S1), STIKI – MALANG, Pembimbing: Evy Poerbaningtyas.

Kata Kunci: Arduino, Sensor HC-SR04, blind spot

Peningkatan kewaspadaan dalam berkendara salah satunya dengan mendeteksi titik buta pengendara.  Saat ini, untuk pengembangan teknologi Arduino pada kendaraan roda 4 atau mobil. Dalam hal keselamatan saat berkendara, terutama untuk mendeteksi titik buta pengendara atau blind spot. Namun masih banyak yang belum menerapkannya pada kendaraan roda 2 atau sepeda motor. Sementara, tingkat kecelakaan pengendara sepeda motor termasuk paling tinggi dan penyebab salah satunya adalah karena pengendara tidak dapat melihat objek di titik buta atau blind spot. Penelitian ini dirancang dengan menggunakan Arduino UNO sebagai mikrokontrolernya, sensor HC-SR04 sebagai alat untuk mendeteksi objek pada titik buta pengendara, lalu lampu LED serta buzzer  yang digunakan sebagai notifikasi untuk pengendara ketika sensor HC-SR04 mendeteksi objek pada titik buta pengendara. Tahapan inti dalam perancangan penelitian ini mencakup analisa perangkat keras, perangkat lunak, perakitan, pengemasan, pemrograman, dan uji coba. Dari penelitian ini menghasilkan, bahwa sensor HC-SR04 dapat mendeteksi objek pada titik buta pengendara dengan baik dengan lampu LED dan buzzer sebagai notifikasi untuk pengendara yang dapat membuat pengendara lebih berhati-hati dan waspada dalam berkendara. Tujuan penelitian ini  menghasilkan sebuah teknologi, dimana dapat membantu meningkatkan keselamatan dan keamanan para pengendara sepeda motor.

# ABSTRACT

Priambodo Budi Santoso, 2022. Detecting Blind Spots on Motorcycle Rider using Arduino Microcontroller with HC-SR04 Sensor. Final Project, Study Program Teknik Informatika S1, STIKI – MALANG, Advisor 1 : Evy Poerbaningtyas.

Keyword: Arduino, HC-SR04 sensor, blind spot

One of the ways to increase awareness in driving is by detecting the driver's blind spots. Currently, for the development of Arduino technology on 4-wheeled vehicles or cars. In terms of safety when driving, especially to detect the driver's blind spot or blind spot. However, there are still many who have not applied it to 2-wheeled vehicles or motorcycles. Meanwhile, motorcyclist accidents are among the highest and one of the causes is that the rider cannot see objects in the blind spot. This research was designed using Arduino UNO as the microcontroller, the HC-SR04 sensor as a tool to detect objects at the driver's blind spot, then the LED lights and buzzer which are used as notifications for the driver when the HC-SR04 sensor detects an object at the driver's blind spot. The core stages in this design include hardware analysis, software, assembly, packaging, programming, and testing. From this research, it is found that the HC-SR04 sensor can detect objects in the driver's blind spot well with LED lights and buzzers as notifications for drivers which can make drivers more careful and alert while driving. The purpose of this research is to produce a technology, which can help improve the safety and security of motorcycle riders.